ORBITER Configuration

Copyright (c) 2000-2022 Martin Schweiger	Sunday 17 July 2022
Orbiter home: orbit.medphys.ucl.ac.uk

# Introduction
This document contains information about the various file formats used by Orbiter, including configuration, scenario and mesh files. Orbiter functionality can be modified and extended by editing or adding new configuration files, e.g. to define a new spacecraft type, or to modify its visual appearance.
# Orbiter configuration files
Configuration files allow the customisation of various aspects of the simulator. Configuration files have file extension .cfg. They are ASCII text files which can be edited with any text editor capable of writing plain text files (e.g. notepad).
Each line contains an item and its value, using the format
<item> = <value>
A semicolon starts a comment, continuing to the end of the line.
All configuration files except the main configuration file (see below) are located in a subdirectory tree defined by the ConfigDir entry in the main file, usually “.\Config”.
## Main configuration file
The main configuration file Orbiter.cfg is located in the Orbiter main directory. It contains general settings for graphics modes, subdirectory locations, simulation parameters, etc. Most of the options in this file are accessible via the Orbiter Launchpad dialog, and manual editing of the file should rarely be necessary.
Orbiter overwrites the main configuration file at the start and end of each simulation session, to store any changes made by the user in the Launchpad dialog.
Normally, only entries whose values differ from their default setting are written to Orbiter.cfg. To force Orbiter to write out all values (useful for debugging or manually editing the file), open Orbiter.cfg in a text editor, change the value of EchoAllParams to TRUE, and save. Subsequently, Orbiter will write all configuration entries to the file.
Item	Type	Description
EchoAllParams	Bool	If TRUE, Orbiter writes all configuration parameters to Orbiter.cfg, including defaults. Default: FALSE
LPadRect	Rect	Screen position of the launchpad dialog window (pixels)
Subdirectory locations
ConfigDir	String	Subdirectory for configuration files. Default: .\Config\
MeshDir	String	Subdirectory for mesh files. Default: .\Meshes\
TextureDir	String	Subdirectory for textures. Default: .\Textures\
HightexDir	String	Subdirectory for alternative high-resolution planetary textures. Default: .\Textures2\
ScenarioDir	String	Subdirectory for scenarios. Default: .\Scenarios\
Logical parameters
StartPaused	Bool	Suspend simulation on launch. Default: FALSE
FlightModel	Int	Flight model realism level. Currently supported: 0 (simple) and 1 (complex). Default: 1
DamageModel	Int	Damage realism level. Currently supported: 0 (no damage) and 1 (damage modelling enabled). Default: 0
UnlimitedFuel	Bool	Ignore spacecraft fuel consumption. Default: FALSE
RefuelOnPad	Bool	Auto-refuel spacecraft parked on a landing pad. Default: TRUE
MFDTransparent	Bool	Make multifunctional displays transparent in “glass cockpit” mode. Default: FALSE
CompactGlasspit	Bool	On widescreen formats, keep MFD displays in the screen centre. Default: TRUE
GenericMFDSize	Int	Scaling factor for MFD displays in “glass cockpit” mode. Supported values: 1–10. Default: 6
MFDMapVersion	Int	Display style for Map MFD mode (0 = old, 1 = new). Default: 1
InstrumentUpdate­Interval	Float	Interval between MFD display updates [s]. Default: 1.0
PanelScale	Float	Scaling factor for instrument panel display. Default: 1.0
PanelScrollSpeed	Float	Speed factor for panel scrolling [pixels/s]. Default: 300.0
User interface parameters
FocusFollowsMouse	Bool	If TRUE, dialog windows receive input focus when the mouse moves over them. Default: TRUE
MenubarMode	Int	Main menu mode (0 = on, 1 = off, 2 = auto-hide). Default: 2
MenuLabelOnly	Bool	Disable main menu icon display. Default: FALSE
ShowWarpAlways	Bool	Display time acceleration even if menubar is hidden. Default: TRUE
ShowWarpScientific	Bool	Display time acceleration in scientific mode. Default: FALSE
InfobarMode	Int	Info bar mode (0 = on, 1 = off, 2 = auto-hide). Default: 0
InfoAuxIdx	Int Int	Auxiliary info box modes left/right. Default: 0 0
MenubarOpacity	Int	Main menu opacity (0–10). Default: 4
InfobarOpacity	Int	Info bar opacity (0–10). Default: 4
MenubarSpeed	Int	Menu/info bar scroll speed (1–20). Default: 10
Visual parameters
EnableShadows	Bool	Enable object shadows on planet surfaces. Default: TRUE
EnableVesselShadows	Bool	Enable vessel shadows on planet surfaces. Default: TRUE
EnableClouds	Bool	Enable rendering of planetary cloud layers. Default: TRUE
EnableCloudShadows	Bool	Enable rendering of cloud shadows on the ground (also requires CloudShadowDepth < 1 in individual planet config files). Default: FALSE
EnableNightlights	Bool	Enable rendering of night lighting effects on planetary surfaces. Default: TRUE
EnableWaterReflection	Bool	Enable rendering of specular reflections from water surfaces. Default: TRUE
EnableSpecularRipples	Bool	Enable microtextures on water surfaces for ripple effects. Default: FALSE
EnableHorizonHaze	Bool	Enable rendering of atmospheric effects at the horizon. Default: TRUE
EnableDistanceFog	Bool	Enable distance-dependent fog effects. Default: TRUE
EnableSpecular­Reflection	Bool	Enable specular reflection effects from polished surfaces Default: TRUE
EnableReentryFlames	Bool	Enable shockwave effects during reentry. Default: TRUE
EnableParticleStreams	Bool	Enable particle generation for exhaust and reentry effects. Default: TRUE
EnableLocalLights	Bool	Enable localised point and spot light emitters. Default: FALSE
MaxLights	Int	Max. simultaneously active lights (0 = query device). Default: 0
AmbientLevel	Int	Ambient light level (brightness of not directly lit surfaces). (0–255). Default: 10
PlanetMaxPatchLevel	Int	Max. texture resolution for planetary surfaces (1–14). Default: 14
PlanetPatchRes	Float	Texture resolution bias for planet surfaces (0.1–10.0). Higher values result in higher render resolution at a given apparent radius, but reduce performance. Default: 1.0
NightlightBrightness	Float	Brightness level of night lighting effects (0.0–1.0). Default: 0.5
StarPrm	List	Brightness and scaling parameters for stars rendered as pixels. Values: app. mag. limit for brightest stars / app. mag. limit for faintest stars / render brightness for faintest stars / lin-log scaling flag. Default: [0.0 7.0 0.1 0]
CSphereBgImage	String	File name for celestial sphere background image. Default: <none>
CSphereBgPath	String	File path to celestial sphere background image.
CSphereBgIntensity	Float	Brightness of background image (0.0–1.0). Default: 0.5
Screen capture parameters
CaptureTarget	Int	0 = clipboard, 1 = file. Default: 0
CaptureFile	String	File name for next screen capture
CaptureSequenceDir	String	Directory name for next screen capture sequence
CaptureImageFormat	Int	0 = BMP, 1 = PNG, 2 = JPG, 3 = TIFF
CaptureImageQuality	Int	1–10
CaptureSequenceStart	Int	Number of next file in sequence
CaptureSequenceSkip	Int	Number of frames to skip in sequence recording
Instrument parameters
ForceMfdPow2	String	TRUE = MFD sizes are set to powers of 2; FALSE = sizes can be arbitrary; AUTO = Orbiter guesses from display caps.
MfdHiresThreshold	Int	MFD threshold size for switching from 256×256 to 512×512 pixels (only used if Pow2 size is active)
Visual helper parameters
Planetarium	Int	Bit flags for display elements in “Planetarium” mode (F9). Default: 4330.
BodyForces	List	Display parameters for force vector visualisation. Values: bit flags for force types / vector scale factor / opacity. Default: [60 1.0 1.0]
CoordinateAxes	List	Display parameters for object axis visualisation. Values: bit flags for object types / axis scale factor / opacity. Default: [4 1.0 1.0]
Debugging options
ShutdownMode	Int	Simulation shutdown method (0 = dealloc memory, 1 = respawn, 2 = terminate). Default: 0
FixedStep	Float	Fixed time interval per frame [s]. Default: 0 (disable fixed frame intervals)
TimerMode	Int	Simulation timer mode (0 = auto, 1 = hires hardware timer, 2 = lores software timer). Default: 0
DisableFontSmoothing	Bool	Turn off font smoothing while running Orbiter to improve performance. Default: TRUE
ForceReenableFont­Smoothing	Bool	Re-enable font smoothing on closing Orbiter even if it was not active at program start. Default: FALSE
HtmlScnDesc	Int	Use inline Html viewer for Launchpad scenario descriptions. 0 = no, 1 = yes, 2 = auto (off for Linux/Wine)
SaveExitScreen	Bool	Take screenshot on session exit to display in scenario description. Default: TRUE
Physics engine
DistributedVesselMass	Bool	Enable gravity gradient torque effects as result of anisotropic inertia tensor. Default: FALSE
NonsphericalGravity­Sources	Bool	Enable orbit perturbations due to nonspherical gravitational potentials. Default: FALSE
RadiationPressure	Bool	Enable orbit perturbations due to radiation pressure. Default: FALSE
StabiliseOrbits	Bool	Use Encke’s method for improved state propagation stability at large time steps. Default: TRUE
StabilisePLimit	Float	Field perturbation limit for orbit stabilisation. Default: 0.05
StabiliseSLimit	Float	Fractional orbit step limit for orbit stabilisation. Default: 0.01
PertPropSubsampling	List	Orbit stabilisation subsampling parameters. Values: max. steps / fractional orbit step limit. Default: [10 0.02]
PertPropNonspherical­Limit	Float	Fractional orbit step beyond which nonspherical gravity effects are ignored. Default: 0.05
PropStages	Int	Number of integrator stages for vessel propagation (1–5). Default: 4
PropStage<i>	List	Integrator parameters for propagator stage <i> (0–4). Values: integrator index / time step limit. Default: i = 0: [2 0.5], i = 1: [4 20.0], i = 2: [6 100.0], i = 3: [8 N/A]
PropSubsampling	Int	Max. subsampling steps. Default: 100
PlanetPreloadMode	Int	Planetary texture load mode. 0 = load on demand, 1 = preload at simulation start. Default: 0
PlanetTexLoadFreq	Float	Texture patch loading frequency [Hz]. Default: 20
PlanetAnisoMode	Int	Planet anisotropic filter level (1 = none). Default: 1
PlanetMipmapMode	Int	Planet texture mipmap mode (0 = none, 1 = point sampling, 2 = linear interpolation). Default: 1
PlanetMipmapBias	Float	Mipmap level bias (−1.0 – +1.0), where < 0 is sharper, > 0 is smoother. Default: 0
Map dialog parameters
MapDlgFlag	Int	Bitflags for map dialog parameter settings
Camera parameters
CameraPanspeed	Float	Camera speed in ground observer mode. Default: 100
HUDColIdx	Int	HUD colour index. Default: 0 (green)
Device settings
DeviceIndex	Int	Enumeration index for current 3D device (do not edit manually)
ModeIndex	Int	Screen mode index (do not edit manually)
DeviceForceEnum	Bool	If TRUE, enumerate 3D devices at each start. Default: TRUE
Fullscreen	Bool	TRUE for fullscreen mode, FALSE for windowed mode. Default: FALSE
Stereo	Bool	Currently not used
NoVSync	Bool	Disable vertical refresh synchronisation. Default: FALSE
StencilBuffer	Bool	Use stencil buffering for semi-opaque shadows, if supported. Default: FALSE
FullscreenPageflip	Bool	Enable hardware page-flipping in fullscreen mode. Default: TRUE
WindowWidth	Int	Horizontal window size for windowed modes [pixel]
WindowHeight	Int	Vertical window size for windowed modes [pixel]
Joystick parameters
JoystickIndex	Int	Enumeration index for current joystick (0 = none). Default: 0
JoystickThrottleAxis	Int	Axis index for joystick throttle (0 = Z, 1 = slider 0, 2 = slider 1). Default: 1
JoystickThrottle­Saturation	Int	Saturation zone for joystick throttle control (0–10000). A setting of 9000 means that the throttle will saturate over the last 10% of its range at either end. Default: 9500
JoystickDeadzone	Int	Deadzone at joystick axis centres (0–10000). A setting of 2000 means that the joystick is considered neutral within 20% from the central position. Default: 2500
IgnoreThrottleOnStart	Bool	Ignore throttle at simulation start until moved. Default: TRUE
Demo parameters
DemoMode	Bool	Start Orbiter in demo mode (auto-launch scenarios). Default: FALSE
BackgroundImage	Bool	Cover screen background with an image in demo mode. Default: FALSE
BlockExit	Bool	Don’t allow users to exit Orbiter in demo mode. Default: FALSE
MaxDemoTime	Float	Max simulation runtime in demo mode [s]. Default: 300
MaxLaunchpadIdleTime	Float	Max. time for launchpad to be open before auto-launching a scenario [s]. Default: 15
Record/play parameters
RecordPosFrame	Int	Flight recorder: reference frame for position data (0 = ecliptic, 1 = equatorial). Default: 1
RecordAttFrame	Int	Flight recorder: reference frame for attitude data (0 = ecliptic, 1 = equatorial). Default: 1
RecordTimeWarp	Bool	Save time acceleration events in recording stream. Default: TRUE
RecordFocusEvent	Bool	Save vessel focus changes in recording stream. Default: TRUE
ReplayTimeWarp	Bool	Set time acceleration during playback from stream data. Default: TRUE
ReplayFocusEvent	Bool	Set vessel focus during playback from stream data. Default: TRUE
ReplayCameraEvent	Bool	Set camera parameters during playback from stream data. Default: TRUE
SystimeSampling	Bool	Use system time (rather than simulation time) for recording sample intervals. Default: TRUE
PlaybackNotes	Bool	Display onscreen annotations from stream during playback. Default: TRUE
Font parameters
DialogFont_Scale	Float	Scaling factor for dialog font size. Default: 1.0
DialogFont1_Face	String	Standard dialog font face. Default: Arial
Window positions
DlgXXXPos	Rect	Screen positions of dialog windows
LpadXXXListWidth	Int	Width of Launchpad splitter lists
Modules list
ActiveModules	List	List of active plugin modules

## Planetary systems
Planetary systems contain stars, planets and moons. Each planetary system requires at least one star. Stars, planets and moons are defined in the planetary system’s configuration file
.\Config\<Solsys-name>.cfg
Orbiter can support multiple planetary systems, but only one per scenario. The planetary system to be used by a scenario is referenced in the scenario file (see Chapter 3).
### General parameters
Item	Type	Description
Name	String	A name for the planetary system
MarkerPath	String	Directory path containing surface marker lists for the planet. Default: .\Config\<Solsys-name>\Marker\

The MarkerPath entry is used only for legacy-style marker definitions (see Chapter 2.5). For new quadtree-based markers, see Planetary Textures, Chapter 9 “Label tile format”.
### Object list
The object list defines the celestial bodies populating the planetary system and their hierarchy.
Star entries:
Star<i> = <Name>
where <i> is an index running from 1 upward. (Note: planetary systems with more than one central star are not currently supported).
Planet entries:
Planet<i> = <Name>
where <i> is an index running from 1 upward.
Moon entries:
<Planet>:Moon<i> = <Name>
where <Planet> is the name of a planet defined before, and <i> is an index enumerating the moons of this planet, running from 1 upward.
Example:
Star1 = Sun
Planet1 = Mercury
Planet2 = Venus
Planet3 = Earth
Earth:Moon1 = Moon
Planet4 = Mars
Mars:Moon1 = Phobos
Mars:Moon2 = Deimos
## Planets
Adding a new celestial body (planet or moon) to a planetary system requires the following steps:
- Add an entry for the body in the planetary system configuration file (see previous chapter).
- Create a configuration file for the planet, defining its orbital, physical and visual parameters, located in .\Config\<Planet-name>.cfg, for example, Config\Earth.cfg. The configuration entries are described below.
- Create the required surface texture maps, and optionally elevation, night light, water mask, cloud layer and feature label maps. See document PlanetTextures.pdf for details.
- Optionally, create configuration files for surface bases in .\Config\<Planet-name>\Base and reference them in the planet configuration file. See Chapter 2.4 for details on surface base definitions.
- Optionally, compile a DLL module for the planet for ephemeris calculations and atmospheric parameter computation. See the Orbiter sources for examples, e.g. the Src\Celbody\Vsop87 project.
- Optionally, create polyline definitions for coastlines (.\Config\<Planet-name>\Data\coast.vec) and/or topography (.\Config\<Planet-name>\Data\contour.vec) to be used in scalable map displays. See .\Config\Earth\Data\coast.vec for an example.
The components of the planet configuration file are listed below. An example for a configuration file can be found in .\Config\Earth.cfg.
### General parameters
Item	Type	Description
Name	String	Planet name
Module	String	Name of a dynamic link library performing calculations for the planet. Default: none
ErrorLimit	Float	Max. rel. error for position/velocity calculations (only used if the module supports precision adjustment)
EllipticOrbit	Bool	If TRUE, use analytic 2-body solution for planet position/velocity calculation, otherwise update dynamically (ignored if module supports position/velocity calculation)
HasElements	Bool	If TRUE, the initial position/velocity is calculated from the provided set of orbital elements, otherwise from an explicit position/velocity pair (ignored if the module supports posi­tion/velocity calculation)

Notes:
If the module calculates the planet position and velocity from a numerical series expansion solution, the value of ErrorLimit affects the number of terms used for the calculation. A lower value increases the number of terms required to achieve that limit, and thus increases calculation time. The valid range for ErrorLimit depends on the module, but is typically 10−3 ≤ ErrorLimit ≤ 10−8.
### Orbital parameters
Ignored if a module is active that supports position/velocity calculation or if HasElements = FALSE.
Item	Type	Description
Epoch	Float	Orbital element reference epoch (e.g. 2000)
ElReference	Flag	Orbit reference frame (ParentEquator or Ecliptic). Default: Ecliptic
SemiMajorAxis	Float	Orbit semi-major axis a [m]
Eccentricity	Float	Orbit eccentricity e.
Inclination	Float	Orbit inclination against reference frame i [rad]
LongAscNode	Float	Longitude of ascending node Ω [rad]
LongPerihelion	Float	Longitude of periapsis ϖ [rad]
MeanLongitude	Float	Mean longitude l at epoch [rad]

### Physical parameters
Item	Type	Description
Mass	Float	Planet mass [kg]
Size	Float	Mean planet radius [m]

### Rotation and precession elements
See also Doc\Technotes\precession.pdf.
Item	Type	Description
SidRotPeriod	Float	Sidereal rotation period [s]. Default: infinite
SidRotOffset	Float	Rotation at epoch [rad]. Default: 0
Obliquity	Float	Obliquity of axis: angle between planet axis and precession reference axis [rad]. Default: 0
LAN	Float	Longitude of ascending node of equatorial plane [rad]. Default: 0
LAN_MJD	Float	Reference data for LAN [MJD]. Default: 51544.5
PrecessionPeriod	Float	Period of precession of axis [days]. Default: infinite
PrecessionObliquity	Float	Obliquity of precession reference axis with respect to ecliptic north pole at J2000 [rad]. Default: 0
PrecessionLAN	Float	Longitude of ascending node of precession reference plane [rad]. Default: 0

### Atmospheric parameters
Only required if the planet defines an atmosphere.
Item	Type	Description
AtmPressure0	Float	(Mean) atmospheric pressure at zero altitude (reference radius) [Pa]
AtmDensity0	Float	(Mean) atmospheric density at zero altitude [kg/m3]
AtmGasConstant	Float	Specific gas constant [J K−1 kg−1]. Default: 286.91 (Earth value)
AtmGamma	Float	Ratio of specific heats cp/cv. Default: 1.4 (Earth value)
AtmColor0	Vec3	RGB triplet for atmospheric colour at ground level (0–1 each)
AtmAltLimit	Float	Altitude limit beyond which atmospheric effects can be ignored [m]
AtmHazeExtent	Float	Width parameter for extent of horizon haze rendering. Range: 0 (thinnest) to 1 (widest). Default: 0.1
AtmHazeShift	Float	Shift the reference altitude of the haze base line (in units of planet radius). Can be used to adjust haze altitude to a cloud layer. Default: 0 (align with surface horizon). Shift is not applied if camera is below cloud layer.
AtmHazeDensity	Float	Modify the density at which the horizon haze is rendered (basic density is calculated from atmospheric density). Default: 1.0
AtmHazeColor	Vec3	RGB triplet for horizon haze colour (0–1 each). Default: use AtmColor0 values.
AtmFogColor	Vec3	RGB triplet for distance fog colour (0–1 each).
AtmFogParam	Vec3	Value 1: fog density at surface level / Value 2: fog density at reference altitude / Value 3: reference altitude [m]
AtmTintColor	Vec3	RGB triplet for additive colour component (0–1 each) added to surface rendering at high altitude
AtmHorizonAlt	Float	Altitude scale for horizon haze rendering [m]. Default: 0.01 of planet radius.
ShadowDepth	Float	Depth (“blackness”) of object shadows (0–1, where 0 = black, 1 = no shadows). Default: exp(−ρ0/2), where ρ0 is atmospheric density at the surface. This option is only used when stencil buffering is enabled, otherwise shadows are always black.

### Cloud parameters
Only required if the planet defines a cloud layer.
Item	Type	Description
CloudFormat	Int	1 = legacy, 2 = 2016 format. Default: 1
CloudAlt	Float	Altitude of cloud layer [m]
CloudShadowDepth	Float	Depth (“blackness”) of cloud shadows on the ground (0–1, where 0 = black, 1 = don’t render shadows). Default: 1
CloudRotPeriod	Float	Rotation period of cloud layer against surface [s]. Default: 0 (static cloud layer)
CloudMicrotextureAlt	Float Float	Altitude range for cloud microtexturing. / Value 1: altitude at which full microtexturing is applied. / Value 2: altitude at which microtexture starts to kick in / Value 1 ≥ 0 and Value 2 > Value 1 is required. Default: no microtexture
BrightenClouds	Bool	Use a brighter cloud rendering algorithm

### Visualisation parameters
Item	Type	Description
TileFormat	Int	1 = legacy, 2 = 2016 format. Default: 1
MaxPatchResolution	Int	Max. resolution level for surface texture maps (1–19)
MinCloudResolution	Int	Min. resolution at which clouds are rendered as a separate layer (1–8)
MaxCloudResolution	Int	Max. cloud resolution level (MinCloudResolution – 19)
MinElevation	Float	Min. surface elevation rel. to planet mean radius [m]. Used to adjust lower edge of rendered horizon.
SpecularRipple	Bool	If TRUE, and if “Specular ripples” option is enabled in the Launchpad dialog, specularly reflecting surfaces use a “water ripple” microtexture. Default: FALSE

### Surface marker parameters (optional)
Item	Type	Description
MarkerPath	String	Directory path to surface marker files for the planet. Default: .\Config\<Planet-name>\Marker\

This entry refers to legacy surface markers (see Chapter 2.5). For new quadtree-based marker definitions, see Planetary Textures, Chapter 9 “Label tile format”.
### Surface bases (optional)
This is a list containing the names and locations of surface landing installations (“spaceports”). Each entry in the list must be accompanied by a configuration file for the corresponding surface base (see Chapter 2.4).
BEGIN_SURFBASE
<base list>
END_SURFBASE
Base list entries have the following format:
<name> <lng> <lat>
where
<name>	Name identifying the base config file (<name>.cfg). The actual base name as it appears in Orbiter is given by the NAME tag in the base config file.
<lng> <lat>	Base centre position in equatorial coordinates [deg]
### Ground-based observer sites (optional)
This is a list containing the pre-defined locations for ground-based observers (launch cameras, spectators, etc.) which can be selected in the Camera dialog. The format of the list is
BEGIN_OBSERVER
<observer list>
END_OBSERVER
List entries have the following format:
<site>:<spot>: <lng> <lat> <alt>
where
<site>	Name identifying the site (e.g. KSC)
<spot>	The particular location at the site (e.g. Launch pad 39A)
<lng> <lat>	Observer position in equatorial coordinates [deg]
<alt>	observer altitude (> 0) [m]
The easiest way to find the coordinates for a new observer spot is to open the Camera dialog (), and select a nearby location under the Ground tab. Then move the camera to the new spot using  and . The coordinates are displayed in the dialog and can be directly copied into the configuration file.
### Navbeacon transmitter list (optional)
This is a list containing the specs of all navigation radio transmitters on the planet surface except for those directly associated with a spaceport, which are defined in the base definition file (see Chapter 2.4). The list format is as follows:
BEGIN_NAVBEACON
<NAV list>
END_NAVBEACON
List entries defining individual transmitters have the following format:
<type> <id> <lng> <lat> <freq> [<range>]
where
<type>	transmitter type, currently supported: VOR
<id>	identifier code (up to 4 characters)
<lng> <lat>	transmitter position in equatorial coordinates [deg]
<freq>	transmitter frequency [MHz]
<range>	transmitter range [m]. Default: 500 000
## Surface bases
Surface bases (or “spaceports”) are launch and landing sites on the surface of planets or moons, usually equipped with launchpads or runways, for vertical and horizontal take-off and/or landing. Each surface base is defined in its own configuration file. When Orbiter loads a planet configuration, it scans all surface base definitions and creates the corresponding bases.
### Base definition file
Each surface base must be defined with a base configuration file. By default, this will be located in
.\Config\<Planet-name>\Base\<Base-name>.cfg
where <Planet-name> is the name of the celestial body the base is located on, and <Base-name> is the name of the surface base. Different locations for the base folder can be defined, for example to allow selective base loading (see Linking surface bases to planets below).
The format of the surface base definition file is as follows:
BASE-V2.0
NAME = <Base-name>
LOCATION = <lng> <lat>
SIZE = <size>
OBJECTSIZE = <osize>
MAPOBJECTSTOSPHERE = [TRUE|FALSE]

BEGIN_NAVBEACON
<NAV list>
END_NAVBEACON

BEGIN_OBJECTLIST
<Object list>
END_OBJECTLIST

BEGIN_SURFTILELIST
<Surface tile list>
END_SURFTILELIST
where
BASE-V2.0
Format identifier (must be placed in the first line of the file). This item is optional if the base is defined directly in the planet’s base list.
NAME = <Base-name>
Logical name of the base as it will be displayed by Orbiter. Doesn’t need correspond to the base file name.
LOCATION = <lng> <lat>
The position of the base reference point on the planet surface, where <lng> [deg] is longitude (< 0 for west, >0 for east), and <lat> [deg] is latitude (< 0 for south, > 0 for north). This item is optional if the base is defined directly in the planet’s base list.
SIZE = <size>
Specifies the size of the base’s footprint on the planet surface (defined as its mean radius [m]. This parameter determines the camera distance at which Orbiter will start rendering the base.
OBJECTSIZE = <osize>
Defines the “typical” size of individual base objects (buildings, etc.). In addition to the SIZE parameter, this value is used by Orbiter to fine-tune the rendering of base objects. Objects will not be rendered if the apparent size of an object of size <osize> located at the base reference point, would be smaller than 1 pixel. The default value for <osize> is 100.0.
MAPOBJECTSTOSPHERE = [TRUE|FALSE]
If TRUE, the altitude of objects in the object list will be adjusted automatically to map them from a flat plane onto a spherical planet surface. So for example, a building defined with altitude 0 will be rendered at altitude 0 relative to the planet’s reference sphere. If FALSE, elevation 0 maps onto the flat plane tangential to the base reference point (and therefore to a point above the reference sphere for any objects not located at the reference point). Default: FALSE
Note: Currently this function is only implemented for a limited number of base object types.
<NAV list>
Contains a list of navigation radio transmitters associated with the base. The format of the list is identical to the <NAV list> in the planet configuration file (see Chapter 2.3).
<Object list>
Contains a list of objects which make up the visual elements of the base. See next section for details.
<Surface tile list>
This list is deprecated and is only retained for backward compatibility of old planet definitions. See document PlanetTextures.pdf for details on how to define surface textures for new planet definitions, including high-resolution patches around surface bases.
### Linking surface bases to planets
After creating the base configuration file, it must be referenced by a planet to instantiate the base. There are several ways to make Orbiter read a surface base definition:
- Place the base configuration file in the default base configuration folder for the planet. By default, Orbiter scans the folder .\Config\<Planet-name>\Base for base definitions. The default folder is scanned only if the planet doesn’t explicitly define a base list (see below).
- To make Orbiter scan different folders, create a surface base list in the planet’s configuration file, enclosed by BEGIN_SURFBASE and END_SURFBASE tags (see Chapter 2.3). In this list, specify the new surface base directory with the line ‘DIR <folder>’, where <folder> is the path to the folder containing the base configurations (relative to the Config folder). Multiple folders can be specified. If the same base is defined in more than one of the scanned folders, only the first is used. This allows to replace base definitions without having to delete the original configuration file. Example:
BEGIN_SURFBASE
DIR Earth\MyBases
DIR Earth\MoreBases
END_SURFBASE
If the surface base list exists in a planet’s configuration file, the default base configuration folder is not scanned, unless it is explicitly listed.
Base references can be placed directly into the base list, using the following format:
<Base-name>:<lng> <lat>
where <Base-name> is the name of the base configuration file, .\Config\<Base-name>.cfg, and <lng> and <lat> are the equatorial coordinates (longitude and latitude) of the base reference point in degrees. This position supersedes the one defined in the base configuration file, so the same base can be used in multiple locations. When using this format, the base configuration file must be located in the .\Config folder.
### Selective loading of bases
To provide more control over the loading of surface bases in a specific simulation scenario, two conditional flags can be set with a DIR entry in the base list:
Specify a time interval with the PERIOD parameter. The corresponding directory is only scanned if the scenario start date is inside this interval. This allows to add or replace surface bases only during specific time periods, for example to set up Kennedy Space Center for the Apollo lunar missions. Syntax:
DIR <folder> PERIOD <MJD0> <MJD1>
where <MJD0> and <MJD1> are the start and end dates of the period over which the base folder is scanned, in MJD (Modified Julian Date) format [days]. Either can be set to ‘–’ to disable the limit at one end.
Specify a scenario context with the CONTEXT parameter. The corresponding directory is scanned only if the scenario specifies the same context string in its environment context entry (see Chapter 3). This allows to add or replace bases only within a defined set of scenarios. Syntax:
DIR <folder> CONTEXT <string>
where <string> is the context string to be matched against the scenario context.
The PERIOD and CONTEXT parameters can be used simultaneously. In that case the directory is only scanned if both conditions are satisfied. Examples:
BEGIN_SURFBASE
DIR Earth\1969Base PERIOD 40222 42048
DIR Earth\TempBases CONTEXT RichScenery
DIR Earth\OtherBases PERIOD - 40000 CONTEXT EarlyBases
DIR Earth\Base
END_SURFBASE
Note that the list order is important to allow the custom base definitions to replace standard bases in the Base subfolder.
### Adding objects to surface bases
Surface bases are composed of objects (buildings, hangars, launch pads, train lines, etc.) The configuration file for each surface base contains a list of its objects:
BEGIN_OBJECTLIST
<Object 0>
<Object 1>
...
END_OBJECTLIST
Each object entry in the list defines a particular object and its properties (type, position, size, textures, etc.) An object can either be a pre-defined type or a generic mesh. Each object entry has the following format:
<Type>
<Parameters>
END
Note that textures used by base objects must be listed in the texture list of the Base.cfg configuration file.
The following pre-defined object types are currently supported:
BLOCK
A 5-sided “brick” (without a floor) which can be used as a simple generic building, or as part of a more complex structure. The following parameters are supported:
Parameter	Type	Description
POS	V	Centre of the block’s base rectangle (in local base coordinates) The y-coordinate is the elevation above ground. Default: 0 0 0
SCALE	V	Object size in the three coordinate axes. Default: 1 1 1
ROT	F	Rotation around vertical axis [deg]. Default: 0
TEX1	S F F	Texture name and u, v scaling factors for walls along the x-axis. Default: no texture
TEX2	S F F	Texture name and u, v scaling factors for walls along the z-axis. Default: no texture
TEX3	S F F	Texture name and u, v scaling factors for roof. Default: no texture

(V = Vector, F = Float, S = String)
HANGAR
A hangar-type building with a barrel-shaped roof. The following parameters are supported:
Parameter	Type	Description
POS	V	Centre of the object’s base rectangle (in local base coordinates) The y-coordinate is the elevation above ground. Default: 0 0 0
SCALE	V	Object size in the three coordinate axes. Default: 1 1 1
ROT	F	Rotation around vertical axis [deg]. Default: 0
TEX1	S F F	Texture name and u, v scaling factors for walls. Default: no texture
TEX2	S F F	Texture name and u, v scaling factors for front gate. Default: no texture
TEX3	S F F	Texture name and u, v scaling factors for roof. Default: no texture

(V = Vector, F = Float, S = String)
HANGAR2
A hangar-type building with a tent-shaped roof. The following parameters are supported:
Parameter	Type	Description
POS	V	Centre of the object’s base rectangle (in local base coordinates) The y-coordinate is the elevation above ground. Default: 0 0 0
SCALE	V	Object size in the three coordinate axes. Default: 1 1 1
ROT	F	Rotation around vertical axis [deg]. Default: 0
TEX1	S F F	Texture name and u, v scaling factors for front and back walls. Default: no texture
TEX2	S F F	Texture name and u, v scaling factors for side walls. Default: no texture
TEX3	S F F	Texture name and u, v scaling factors for roof. Default: no texture
ROOFH	F	Roof height from base to ridge. Default: 1/2 building height.

(V = Vector, F = Float, S = String)
HANGAR3
A hangar-type building with a barrel-shaped roof reaching to the ground. The following parameters are supported:
Parameter	Type	Description
POS	V	Centre of the object’s base rectangle (in local base coordinates) The y-coordinate is the elevation above ground. Default: 0 0 0
SCALE	V	Object size in the three coordinate axes. Default: 1 1 1
ROT	F	Rotation around vertical axis [deg]. Default: 0
TEX1	S F F	Texture name and u, v scaling factors for front and back walls. Default: no texture
TEX2	S F F	Texture name and u, v scaling factors for front gate. Default: no texture
TEX3	S F F	Texture name and u, v scaling factors for roof. Default: no texture

(V = Vector, F = Float, S = String)
TANK
A fuel tank-like upright cylinder with a flat top. The following parameters are supported:
Parameter	Type	Description
POS	V	Centre of the object’s base circle (in local base coordinates) The y-coordinate is the elevation above ground. Default: 0 0 0
SCALE	V	Cylinder radii in x and z, and height in y. Default: 1 1 1
ROT	F	Rotation around vertical axis [deg]. Default: 0
NSTEP	I	Number of segments to approximate circle. Default: 12
TEX1	S F F	Texture name and u, v scaling factors for mantle. Default: no texture
TEX2	S F F	Texture name and u, v scaling factors for top. Default: no texture

(V = Vector, F = Float, I = Integer, S = String)
RUNWAY
Texturing for a runway. The texture mapping can be split into segments, to allow the inclusion of markings, overruns, etc. The RUNWAY object does not include any lighting, which is instead provided with the RUNWAYLIGHTS object (see below).
Parameter	Type	Description
END1	V	First end point of the runway (centre line), including any overruns to be textured.
END2	V	Second end point of the runway centre line.
WIDTH	F	Runway width [m]
ILS1	F	Localiser frequency for approach towards END1 [MHz]. Range: 108.00–139.95. Default: no ILS support
ILS2	F	Localiser frequency for approach towards END2. Can be the same frequency as ILS1. Default: no ILS support
NRWSEG	I	Number of texture segments
RWSEGx	I F F F F F	Definition of segment x (x = 1–NRWSEG) / Parameters: / 1. Number of mesh sub-segments (≥ 1) / 2. Fractional length of segment (sum of all segments must be 1) / 3. Texture coordinate u0 of segment / 4. Texture coordinate u1 / 5. Texture coordinate v0 / 6. Texture coordinate v1
RWTEX	S	Texture name for all segments

(V = Vector, F = Float, I = Integer, S = String)
RUNWAYLIGHTS
Complete lighting for a single runway, including optional Precision Approach Path Indicator (PAPI) and Visual Approach Slope Indicator (VASI). Runway markers are turned off during daytime, but PAPI and VASI indicators are always active.
Parameter	Type	Description
END1	V	First end point of the runway (centre line).
END2	V	Second end point of the runway centre line.
WIDTH	F	Runway width [m]
COUNT1	I	Number of lights along the runway centre line (≥ 2). Default: 40
PAPI	F F F	Precision Approach Path Indicator (PAPI). Default: no PAPI / Parameters: / Designated approach descent angle [deg] / Approach cone aperture [deg] / Offset of PAPI location from runway endpoints [m]
VASI	F F F	Visual Approach Slope Indicator (VASI). Default: no VASI / Parameters: / Designated approach descent angle [deg] / Distance between white and red indicator lights [m] / Offset of VASI (red bar) location from runway endpoints [m]

(V = Vector, F = Float, I = Integer)
BEACONARRAY
A linear array of illuminated beacons, usable e.g. for taxiway night lighting.
Parameter	Type	Description
END1	V	First end point of beacon array in local base coordinates. y-coordinate is elevation above ground.
END2	V	Second end point of beacon array.
COUNT	I	Number of beacons in the array (≥ 2). Default: 10
SIZE	F	Size (radius) of each beacon light. Default: 1.0
COL	F F F	Beacon colour (RGB). Range: 0–1 for each value. Default: 1 1 1 (white)

(V = Vector, F = Float, I = Integer)
SOLARPLANT
A grid of ground-mounted solar panels, smart enough to align themselves with the Sun. The following parameters are supported:
Parameter	Type	Description
POS	V	Centre position of the panel grid. Default: 0 0 0
SCALE	F	Scaling factor for each panel. Default: 1.0
SPACING	F F	Distance between panels in x and z directions [m]. Default: 40 40
GRID	I I	Grid dimensions in x and z directions. Default: 2 2
ROT	F	Rotation of plant around vertical axis [deg]. Default: 0
TEX	S [F F]	Texture name and u, v scaling factors for panels. Default: no texture

(V = Vector, F = Float, I = Integer, S = String)
TRAIN1
A monorail-type train on a straight track. The following parameters are supported:
Parameter	Type	Description
END1	V	First end point of track
END2	V	Second end point of track
MAXSPEED	F	Maximum speed of train [m/s]. Default: 30
SLOWZONE	F	Distance over which the train slows down at the track ends [m]. Default: 100
TEX	S	Texture name

(V = Vector, F = Float, S = String)
TRAIN2
Suspended train on elevated straight track. The following parameters are supported:
Parameter	Type	Description
END1	V	First end point of track
END2	V	Second end point of track
HEIGHT	F	Elevation of suspension track over ground [m]. Default: 11
MAXSPEED	F	Maximum speed of train [m/s]. Default: 30
SLOWZONE	F	Distance over which the train slows down at the track ends [m]. Default: 100
TEX	S	Texture name

(V = Vector, F = Float, S = String)
LPAD1
An octagonal bordered landing pad. Default diameter 80 m (at scale 1). Landing pads are numbered in the order they appear in the list. This landing pad style can be assigned numbers 1–9, so must be within the first 9 landing pad definitions of the base object list. Orbiter provides a texture map compatible with LPAD1 (Textures\Lpad01.dds). Any user-defined texture should adhere to the same layout.
Parameter	Type	Description
POS	V	Pad centre coordinates in local base frame.
SCALE	F	Scaling factor. Default: 1
ROT	F	Rotation around vertical axis [deg]. Default: 0
TEX	S	Texture name. Default: no texture
NAV	F	Frequency of VTOL nav transmitter [MHz] (range 85.0–140.0). Default: no transmitter

(V = Vector, F = Float, S = String)
LPAD2
A square landing pad. Default size 80 m (at scale 1). Landing pads are numbered in the order they appear in the list. This landing pad style can be assigned numbers 1–99, so must be within the first 99 landing pad definitions of the base object list. Orbiter provides a texture map compatible with LPAD2 (Textures\Lpad02.dds). Any user-defined texture should adhere to the same layout.
Parameter	Type	Description
POS	V	Pad centre coordinates in local base frame.
SCALE	F	Scaling factor. Default: 1
ROT	F	Rotation around vertical axis [deg]. Default: 0
TEX	S	Texture name. Default: no texture
NAV	F	Frequency of VTOL nav transmitter [MHz] (range 85.0–140.0). Default: no transmitter

(V = Vector, F = Float, S = String)
LPAD2A
Similar to LPAD2, but uses a different layout for the texture map, providing a higher resolution at the same texture size. Orbiter provides a texture map compatible with LPAD2A (Textures\Lpad02a.dds). Any user-defined texture should adhere to the same layout. The supported parameters are the same as for LPAD2.
MESH
Generic mesh for custom objects. Mesh files must be in Orbiter mesh file format (see Chapter xxx).
Parameter	Type	Description
FILE	S	Mesh file name (without path and extension). Mesh files must be located in the mesh subdirectory (as defined in the main config file)
POS	V	Position of the mesh origin in local base coordinates
SCALE	V	Scaling factors in along the 3 axes (height in y). Default: 1 1 1
ROT	F	Rotation around the vertical axis [deg]. Default: 0
TEX	S	Texture name. Default: none
WRAPTOSURFACE		Wrap mesh vertices to the planet surface (e.g. taxiways and similar)
SHADOW		Render the shadow cast on the ground by the object (cannot be used together with OWNSHADOW)
OWNSHADOW		Use group shadow flags in mesh file to set shadows for individual mesh groups (cannot be used together with SHADOW)
UNDERSHADOWS		Object can be covered by shadows cast on the ground by other objects (e.g. roads, landing pads, etc.). Default: object not covered by ground shadows
OWNMATERIAL		Use materials and textures defined in the mesh file. This overrides the TEX entry.
LPAD		Object is a landing pad
PRELOAD		Mesh should be loaded at program start. This can reduce disc activity during the simulation, but increases main memory usage. Default: load only when used.

(V = Vector, F = Float, S = String)
Notes:
- If the mesh only uses a single texture it is more efficient to specify it via the TEX entry instead of defining it in the mesh and using the OWNMATERIAL flag, because Orbiter can merge objects with the same TEX entries for improved performance.
- If OWNSHADOW is used, any mesh groups which have bit 0 set in their FLAG entry do not cast shadows, otherwise they do cast shadows (see Chapter xxx).
## Custom markers
Note: As regards markers for planetary surface featues, this section contains information for old-style (pre-Orbiter 2016) marker definitions. These are retained for backward compatibility. For new, quadtree-based marker definitions, see Chapter Label Tile Format of document PlanetTextures.pdf.
Labels can be defined to mark objects on the celestial sphere (e.g. bright stars, navigation stars, nebulae, etc.) or on planetary surfaces to locate natural landmarks, points of interest, historic landing sites, navigational aids, etc.
The user can display these markers during the simulation with the Visual helpers option ( or ).
By default, all files for celestial and planetary surface markers are placed in a subdirectory
.\Config\<name>\Marker
where <name> is the name of the planetary system (for celestial markers) or the celestial body (for surface markers) they are referring to. A different location for marker files can be specified with the MarkerPath option in the planet’s or planetary system’s configuration file (see Chapters 2.2 and 2.3). Marker files are text files with extension .mkr. Multiple files can be defined for a single planet or planetary system, which the user can turn on and off individually. The format is
BEGIN_HEADER
InitialState [on|off]
ShapeIdx [0–6]
ColourIdx [0–5]
Size [0.1–2]
DistanceFactor [1e−5 – 1e3]
Frame [celestial|ecliptic]
END_HEADER
BEGIN_DATA
<lng> <lat> : <label> [: <label>]
<lng> <lat> : <label> [: <label>]
. . .
The header section contains some configuration options:
- InitialState defines if the labels are initially visible when the user activates surface or celestial markers in the Visual helpers dialog. The user can turn lists on and off individually during the simulation. The default is off.
- ShapeIdx is an integer between 0 and 6 defining the shape of the label markers:
0		box (default)
1	○	circle
2	◊	diamond
3	△	nabla
4	▽	delta
5		crosshair
6		rotated crosshair

ColourIdx is an integer between 0 and 5 defining the colour of the labels:
0		yellow
1		cyan (default)
2		red
3		purple
4		green
5		blue

- Size scales the marker size. Default: 1.0
- DistanceFactor resets the distance up to which camera distance the markers are displayed. Default: 1.0
- Frame (used for celestial markers only) defines the reference to which the coordinates in the list refer:
  - ecliptic: coordinates are ecliptic longitude and latitude
  - celestial: coordinates are right ascension and declination of J2000 equator and equinox
Each item in the header section is optional. If missing, the default value is substituted. The header can also be omitted altogether, in which case the BEGIN_DATA tag is also not required.
In the data section, each line defines a label. It consists of equatorial position: longitude [deg], with eastern longitudes positive and western longitudes negative, latitude [deg], with northern latitudes positive and southern latitudes negative, and one or two label strings to be displayed above and below the marker.
## Vessels
All vessel configuration files are by default located in .\Config\Vessels. Simple vessel types can be defined by their configuration files alone. More complex functions and capabilities require either a compiled vessel module or a script interface.
Below is a description of the default vessel configuration options recognised by Orbiter. Not all options are required, in particular if the vessel is controlled by a module or script (in which case only the Module or Script tags are mandatory). Also, custom vessel modules may read additional non-standard options from the configuration file.
Item	Type	Description
ClassName	String	Vessel class name. Usually the same as the configuration file name.
BaseClass	String	Optional parent class. Missing entries are taken from this class. Allows the construction of class hierarchies. Make sure not to introduce circular dependencies.
Module	String	Optional; name of plugin module for vessel control. The module must be located in the .\Modules subdirectory
EditorModule	String	Optional: name of plugin module containing custom extensions for scenario editor plugin (see ScenarioEditor.pdf). Can be the same as Module
Script	String	For script-based vessels (Module = ScriptVessel) only. Defines the vessel script file (can be the same as the configuration file). See .\Config\Vessels\ScriptPB.cfg for an example.
Help	String, String	Optional: name of help file to be used for vessel class-specific help when the user presses the “Vessel” button in the Help dialog. The help file must be a compiled html file (.chm) and located in directory .\Html\Vessels. The entry contains the file name without path and extension and (separated by comma) the name of the first page to be displayed (without extension). Default: no vessel-specific help
EditorCreate	Bool	If FALSE, the vessel type does not appear in the list of the vessel creation page of the scenario editor. Default: TRUE
ImageBmp	String	File name of a bitmap file (.bmp) displaying the vessel. The name should include the path (relative to the Orbiter main directory) and extension (.bmp). The image is shown in the vessel creation page of the scenario editor. For best results, it should be size 164×240 pixels.
MeshName	String	Name of the mesh file used for vessel visualisation (without .msh file extension, located in .\Meshes subdirectory, or with optional path relative to .\Meshes)
EnableFocus	Bool	If TRUE, vessel can receive input focus. Default: TRUE
EnableXPDR	Bool	TRUE if vessel carries a transponder. Default: FALSE
XPDR	Int	Transponder channel (≥ 0) in units of 0.05 MHz from 108.0 MHz). Only used if EnableXPDR = TRUE.
Mass	Float	Vessel mass (empty) [kg]
Size	Float	Mean vessel radius [m]
ClipRadius	Float	Vessel clip radius [m]. Radius of a sphere enclosing the vessel mesh to avoid visual clipping. Set this to > Size if visual artefacts (clipping) occur when the camera moves close to the vessel. Default: same as Size.
MaxMainThrust	Float	Max. thrust force of main thruster(s) in vacuum [N]
MaxRetroThrust	Float	Max. thrust force of retro thuster(s) in vacuum [N]
MaxHoverThrust	Float	Max. thrust force of hover thruster(s) in vacuum [N]
MaxAttitudeThrust	Float	If provided, this creates a complete set of thrusters for a reaction control system (RCS) to control the vessel’s attitude. The value defines the vacuum thrust [N] of each individual RCS thruster. All thrusters are assumed to have an offset of 1 m from the vessel’s centre of mass, so the thrust value must be scaled accordingly to provide a given target torque.
TouchdownPoints	Vec3 × 3	3 surface contact points in local vessel coordinates. For aircraft-like configurations these are: nose wheel, left main wheel, right main wheel (the order is important to define the ‘up’ direction). Other spacecraft types may interpret the points differently.
CameraOffset	Vec3	Camera position inside the vessel for cockpit view
CW	Float × 4	Airflow resistance coefficients: forward, backward, transversal, vertical. Only used by legacy flight model (if no airfoils are defined in the module).
WingAspect	Float	The wing aspect ratio (wingspan2 / wing area). Used for atmospheric drag calculation in legacy flight model
WingEffectiveness	Float	A wing form factor: ~3.1 for elliptic wings, ~2.8 for tapered wings, ~2.5 for rectangular wings. Only used for legacy flight model.
CrossSections	Vec3	Cross sections in axis directions (z = longitudinal) [m2]
RotResistance	Vec3	Resistance against rotation around axes in atmosphere, where angular deceleration due to atmospheric friction is { dot %omega }_{x, y, z} `=` - %omega_{ x, y, z } %rho r_{ x, y, z } with angular velocity ω and atmospheric density ρ.
Inertia	Vec3	Principal moments of inertia, mass normalised (see below) [m2]
GravityGradient­Damping	Float	Damping coefficient for gravity gradient torque. Determines relaxation time for tidal locking. Default: 0 (undamped)
PropellantResource<i>	Float [Float]	Specs for propellant resource <i> (i ≥ 1). First value: max fuel capacity [kg]. Second value: fuel efficiency factor (> 0, default: 1)
MaxFuel	Float	Max. fuel mass [kg]. Obsolete; only used if no propellant resources are defined.
Isp	Float	Default value for fuel-specific impulse [m/s]: amount of thrust [N] obtained by burning 1 kg of fuel per second. Vessel modules can override this value for individual engines.
MEngineRef<i>	Vec3	Reference position for main thruster <i> (<i> ≥ 1)
REngineRef<i>	Vec3	Reference position for hover thruster <i> (<i> ≥ 1)
HEngineRef<i>	Vec3	Reference position for hover thruster <i> (<i> ≥ 1)
AttRef<d><i><j>	Vec3	Reference position for attitude thruster (for rotation around axis <d> (<d> = x,y,z), rotation direction <i> (<i> = 1,2) and thruster index <j> (<j> = 1,2) for a total of 12 attitude thrusters
LongAttRef<i><j>	Vec3	Reference position for attitude thrusters (for linear forward/backward translation), direction <i> (<i> = 1,2) and thruster index <j> (<j> = 1.2) for a total of 4 attitude thrusters
DockRef	Vec3	Docking reference point for first docking port (obsolete)
DockDir	Vec3	Docking approach direction for first docking port (obsolete)
DockRot	Vec3	Longitudinal alignment direction (normal to DockDir) for first docking port (obsolete)
<Docklist>	List	List of positions and approach directions for docking ports (see below)
<Attachment list>	List	List of positions and approach directions for attachment points (see below)

Notes:
- A vessel class can be derived from a different vessel class by defining the BaseClass entry. All properties not defined in the new class configuration file are taken from the base class.
- The mesh name (MeshName value) does not include the file extension (.msh assumed) or directory path (Orbiter’s mesh directory assumed, by default .\Meshes).
- The MaxFuel entry has been replaced by PropellantResource, which allows the definition of multiple propellant resources (fuel tanks).
- The DockRef, DockDir, DockRot entries have been replaced with the more versatile Docklist, which allows the configuration of multiple docking ports and IDS (instrument docking system) frequencies.
BEGIN_DOCKLIST
<Dock-spec 0>
<Dock-spec 1>
. . .
END_DOCKLIST
where each <Dock-spec i> has the format
<xi> <yi> <zi> <dxi> <dyi> <dzi> <rxi> <ryi> <rzi> [<ids-channeli>]
<xi> <yi> <zi> is the reference position of the docking port in the local vessel frame. <dxi> <dyi> <dzi> is the direction in which a ship approaches the docking port. <rxi> <ryi> <rzi> is a reference direction perpendicular to the approach direction used for aligning an approaching ship’s rotation around its longitudinal axis. <ids-channeli> is an optional channel number (≥ 0) for an IDS transmitter that allows instrument-aided docking approach. IDS frequencies start at 108.0 MHz (channel 0) and increase by 0.05 MHz per channel.
The IDS setting can be overridden for individual vessels by using the IDS tag in the scenario file. Defining the IDS channel in the configuration file is only useful for objects with a single instance, e.g. space stations.
- The attachment list is similar to the docklist: It allows to specify points at which vessels can be connected to each other. Unlike peer-to-peer docking ports, attachment points define parent-child hierarchies, and each attachment point is either a parent or a child port. For more details see the Vessel attachment management section in the API reference manual.
BEGIN_ATTACHMENT
<Attach-spec 0>
<Attach-spec 1>
. . .
END_ATTACHMENT
where each <Attach-spec i> has the format
- <typei> <xi> <yi> <zi> <dxi> <dyi> <dzi> <rxi> <ryi> <rzi> <idi>
  <typei> is a single character: ‘P’ (attach to parent) or ‘C’ (attach to child). The next 9 entries define the attachment position and direction in the same way as docking ports. <idi> is a string of up to 8 characters used for defining compatibility between attachment points.
- The 3 values of the Inertia tag are the principal moments of inertia, defined as the diagonal elements (Jxx, Jyy, Jzz) of the mass-normalised inertia tensor J in the vessel’s principal frame, where J is diagonal. J in an arbitrary frame is given by
  {bold nitalic J} `=` 1 over M int from{V} { m( r ) left [ matrix{y^2 + z^2 # xy # xz ## yx # x^2 + z^2 # yz ## xz # xy # x^2 + y^2} right ] dr }
  The Orbitersdk\Utils folder contains a simple tool (shipedit.exe) to calculate the inertia tensor of an object from its mesh file. The tool requires “well-behaved” mesh files (composed of closed compact surfaces) and assumes a homogeneous density distribution inside the mesh (m(r) = const). The latter is not very realistic, so the results must be interpreted realistically. They should still serve as a good starting point for experimentation.

# Scenario files
Scenarios are simulation startup definitions which contain all parameters required to set up the starting conditions of the simulation at a particular time. They are used for loading and saving simulation states. A scenario file is generated during the simulation when the user saves a state, or automatically at the simulation termination so it can be picked up later.
Scenario files are text files that can be created or modified manually. An easier way to edit scenarios is with the Scenario Editor plugin, which can be used to modify and save a running simulation. The Scenario Editor is described in a separate document (ScenarioEditor.pdf).
Scenario files are located in a subdirectory tree specified by the ScenarioDir entry in the main configuration file (see Chapter 2.1), usually .\Scenarios. They have file extension .scn.
### Format
Scenario files consist of a series of category blocks describing different aspects of the simulation state:
<Description block>
<Environment block>
<Focus block>
<Camera block>
<Panel block>
<VC block>
<HUD block>
<Left MFD block>
<Right MFD block>
<Vessel list>
### Description block (optional):
Contains a short description of the scenario which is presented to the user in Orbiter’s Launchpad dialog window on highlighting the scenario. There are two versions of the description block available:
BEGIN_DESC
<Text-description>
END_DESC
where <Text-description> contains a scenario description in plain text format. The description can span multiple lines. An empty line is converted into a new line on display. More powerful formatting options are available with the alternative
BEGIN_HYPERDESC
<HTML-description>
END_HYPERDESC
where <HTML-description> is passed to an HTML parser for rendering in the Launchpad window and can contain HTML formatting tags such as <h1></h1>, <b></b>, <br>, etc. However, references to external objects, such as images or links, are not allowed. To also use images or hyperlinks to multi-page descriptions, use the HELP tag in the environment block (see below) which supersedes the description block.
### Environment block (optional):
Contains the simulation environment. Format:
BEGIN_ENVIRONMENT
<Environment parameters>
END_ENVIRONMENT
The following environment parameters are supported:
Item	Type	Description
SYSTEM	String	Name of the planetary system. A configuration file for this system must exist (see Chapter 2.2). Default: “Sol”
DATE		Contains the simulation start time. Allowed formats are: / MJD <mjd> (Modified Julian date [days]) / JD <jd> (Julian date) / JE <je> (Julian epoch) / Default is current system time, but this should be avoided if the scenario contains objects defined by position/velocity state vectors at a fixed time, which cannot easily be propagated
HELP	String [,String]	Scenario help file (in HTML or compressed CHM format). For a HTML page, specify the location of the page relative to the Html\Scenarios folder and without extension (.htm is assumed). For a page in a CHM file, specify the location of the file relative to the Html\Scenarios folder without extension (.chm is assumed), followed by a comma and the name of the page inside the file without extension (.htm is assumed). Scenario help files are displayed in the Launchpad scenario tab and can also be opened during the simulation with Alt-F1. Default: no help file
CONTEXT	String	Optional context string. This can be used to fine-tune the setup of a planetary system, e.g. by selective loading of surface bases (see Chapter 2.4).
SCRIPT	String	A script file to launch at the scenario start. The string should include any path relative to the “Script” subdirectory, but no file extension (.lua is assumed). Default: no script

Notes:
- If the DATE entry is not present, Orbiter reads the computer system clock, adds the time zone offset to convert to Universal Time (UTC) and adds another offset of 66.184 seconds to map from UTC to Barycentric Dynamical Time (TDB).
- If the HELP entry is present, the description block is ignored.
- The script launched with the SCRIPT entry can be used for demos, interactive tutorials, etc. For Lua scripting in Orbiter, see .\Orbitersdk\doc\orbiter_lua.chm.
### Focus block:
Contains parameters for the user-controlled spacecraft. Format:
BEGIN_FOCUS
<Focus parameters>
END_FOCUS
with the following parameters supported:
Item	Type	Description
SHIP	String	Name of the user-controlled ship. The ship must be listed in the ship list (see below).

### Camera block (optional):
Camera mode and parameters. If the camera block is missing, the camera is set to cockpit view in the current focus object. Format:
BEGIN_CAMERA
<Camera parameters>
END_CAMERA
with supported parameters
Item	Type	Description
MODE	Flag	Extern | Cockpit (selects external or cockpit camera mode)
TARGET	String	Camera view target object (external modes only, cockpit mode always refers to the current focus object)
POS	Vec3	Camera position relative to target (external modes only)
TRACKMODE	Flag [+String]	TargetRelative | AbsoluteDirection | GlobalFrame | TargetTo <ref> | TargetFrom <ref> | Ground <ref> (external modes only)
GROUNDLOCATION	Vec3	longitude [deg], latitude [deg] and altitude [m] of ground observer (Ground trackmode only)
GROUNDDIRECTION	Float Float	polar coordinates of ground observer orientation (free Ground trackmode only)
FOV	Float	Field of view (angular aperture from from top to bottom of view window) [deg]

### Panel block (optional):
2D instrument panel parameters. If neither this nor the VC block is present, Orbiter initially displays the generic glass cockpit view in internal (cockpit) modes. If both are present, the 2D panel view takes precedence. Format:
BEGIN_PANEL
<Panel parameters>
END_PANEL
Currently no panel parameters are supported, but the presence of the panel block indicates a preference for 2D panel modes on startup, if supported by the focus vessel.
### VC block (optional):
Virtual cockpit parameters. If neither this nor the panel block is present, Orbiter initially displays the generic glass cockpit view in internal (cockpit) modes. Format:
BEGIN_VC
<VC parameters>
END_VC
Currently VC parameters are supported, but the presence of the VC block indicates a preference for virtual cockpit modes on startup, if supported by the focus vessel.
### HUD block (optional):
HUD (head up display) mode and parameters for cockpit views. If the HUD block is missing, no HUD is displayed at simulation start. Format:
BEGIN_HUD
<HUD parameters>
END_HUD
with supported parameters
Item	Type	Description
TYPE	Flag	Orbit | Surface | Docking

### Left/right MFD blocks (optional):
Left and right MFD (multifunctional display) mode and parameters. If an MFD block is missing, the corresponding MFD is switched off. Note that custom MFD modes can define their own set of parameters. If the current cockpit mode supports more than two MFD instruments, only the parameters for the first to are preserved. Format:
BEGIN_MFD [Left | Right]
<MFD parameters>
END_MFD
The following parameters are supported (most of which are relevant only for specific MFD modes):
Item	Type	Description
TYPE	Flag	MFD mode: Orbit | Surface | Map | Launch | Docking | OAlign | OSync | Transfer
REF	String	Reference object (Orbit and Map modes only)
TARGET	String	Target object (Orbit, OAlign, OSync modes only)
BTARGET	String	Base target (Map mode only)
OTARGET	String	Orbit target (Map mode only)
PROJ	Flag	Ecliptic | Ship | Target (Orbit mode only)
MODE	Flag	Intersect 1 | Intersect 2 | Sh periapsis | Sh apoapsis | Tg periapsis | Tg apoapsis | Manual axis (OSync mode only)
MANUALREF	Float	Reference axis position [deg] (OSync mode in manual axis setting only)
LISTLEN	Int	Length or orbit list (OSync mode only)

### Ship list:
A list of all spacecraft in the simulation and their state parameters. The list must contain at least one vessel referenced by the Focus block. Format:
BEGIN_SHIPS
<Ship 0>
<Ship 1>
...
END_SHIPS
where the entry format for each ship is given by
<Vessel name>[: <Class name>]
<Vessel parameters>
END
If both the vessel and class names are present, the vessel is created as an instance of the vessel class, and a configuration file for the vessel class, <Class name>.cfg must exist. If only the vessel name is present, it is assumed to be a soliton (the only representative of its class) and the vessel class is assumed to coincide with its name.
The following generic parameters are supported:
Item	Type	Description
STATUS	Flag	Landed <planet> | Orbiting <planet>
BASE		<base>:<lpad> (only for status Landed)
HEADING	Float	Orientation (only for status Landed)
RPOS	Vec3	Position relative to reference body (only for status Orbiting)
RVEL	Vec3	Velocity relative to reference body (only for status Orbiting)
ELEMENTS	List	Osculating orbital elements. This is an alternative to the state vector specification (RPOS and RVEL) for vessels with status Orbiting. The list contains 7 entries: / semi-major axis a [m], / eccentricity e, / inclination i [deg], / longitude of ascending node Ω [deg], / longitude of periapsis ϖ [deg], / mean longitude at epoch l [deg] / epoch t [MJD]
AROT	Vec3	Orientation: rotation angles of object frame (only for status Orbiting)
VROT	Vec3	Angular velocity [deg/s] (only for status Orbiting)
FUEL	Float	Fuel level (0–1). This tag sets the level of all propellant resources to the same level. For individual settings use PRPLEVEL instead.
PRPLEVEL	List	List of propellant resource levels. Each entry is of the form <id>:<level>, where <id> is the resource identifier (Int ≥ 0) and <level> is the propellant resource level (Float, 0–1)
THLEVEL	List	List of thruster settings. Each entry is of the form <id>:<level>, where <id> is the thruster identifier (Int ≥ 0) in the order of thruster definition and <level> is the thrust level (Float, 0–1). Thrusters with level 0 can be omitted.
DOCKINFO	List	Docking status list. This contains information about all docked vessels. Each entry is of the form <id>:<rid> <rvessel>, where <id> is the docking port identifier (Int ≥ 0), <rid> is the docking port identifier of the docked vessel, and <rvessel> is the docked vessel. Only engaged docking ports are listed. See notes below.

In addition to these generic parameters, individual vessel classes may define class-specific parameters.
Defining docked assemblies:
There are two ways to define vessels as being assembled into a superstructure by docking them together:
- Place the vessels so that their docking point locations coincide (by using the appropriate RPOS, RVEL, AROT and VROT parameters for both). Orbiter will dock two vessels automatically if their docking ports are close enough.
- Define the DOCKINFO lists for both vessels so that they reference each other. Orbiter then attaches the vessels accordingly even if their position parameters are not aligned. In that case, the position of the first vessel in the superstructure list defines the position of the assembly. The position parameters of all subsequent vessels in the list are ignored.
In general it is easier to set up vessel states within the simulation by using the ScenarioEditor plugin and writing out the resulting scenario file than manually editing the file.
# Keyboard function mapping
The keymap.cfg file in the Orbiter root directory contains the key mapping definitions for the default Orbiter functions. Individual vessel classes and other plugins may define additional key functions.
keymap.cfg is a text file and can be edited with any editor capable of writing plain ASCII text files. Each line contains a key definition in the format
<function> = <key>
where <function> is one of the function identifiers listed in the table below, and <key> is a key identifier, optionally followed by one or more modifier keys.
For supported key identifiers, see Chapter Keyboard key identifiers in document Orbitersk\doc\API_Reference.chm. The key identifiers in the format required by keymap.cfg are as defined in the list, minus the OAPI_KEY_ prefix.
Supported modifier keys are LSHIFT, RSHIFT, LCTRL, RCTRL, CTRL, LALT, RALT, ALT.
Missing entries in keymap.cfg are substituted by their default values. To revert to the original key mapping, simply delete keymap.cfg. Orbiter will create a new one the next time it is run.
Function	Default value	Description
CockpitCamRotateLeft	LEFT ALT	Rotate camera left in cockpit mode
CockpitCamRotateRight	RIGHT ALT	Rotate camera right in cockpit mode
CockpitCamRotateUp	UP ALT	Rotate camera up in cockpit mode
CockpitCamRotateDown	DOWN ALT	Rotate camera down in cockpit mode
CockpitCamDontLean	DOWN CTRL ALT	Return camera to default position in VC mode
CockpitCamLeanForward	UP CTRL ALT	Lean forward in VC mode
CockpitCamLeanLeft	LEFT CTRL ALT	Lean left in VC mode
CockpitCamLeanRight	RIGHT CTRL ALT	Lean right in VC mode
CockpitResetCam	HOME	Return to default cockpit camera direction
PanelShiftLeft	LEFT	Scroll 2D panel left
PanelShiftRight	RIGHT	Scroll 2D panel right
PanelShiftUp	UP	Scroll 2D panel up
PanelShiftDown	DOWN	Scroll 2D panel down
PanelSwitchLeft	LEFT CTRL	Switch to left neighbour panel
PanelSwitchRight	RIGHT CTRL	Switch to right neighbour panel
PanelSwitchUp	UP CTRL	Switch to upper neighbour panel
PanelSwitchDown	DOWN CTRL	Switch to lower neighbour panel
TrackCamRotateLeft	LEFT CTRL	Rotate camera left in external track mode
TrackCamRotateRight	RIGHT CTRL	Rotate camera right in external track mode
TrackCamRotateUp	UP CTRL	Rotate camera up in external track mode
TrackCamRotateDown	DOWN CTRL	Rotate camera down in external track mode
TrackCamAdvance	PGDOWN	Move camera closer in external track mode
TrackCamRetreat	PGUP	Move camera away in external track mode
GroundCamTiltLeft	LEFT	Tilt camera left in ground observer mode
GroundCamTiltRight	RIGHT	Tilt camera right in ground observer mode
GroundCamTiltUp	UP	Tilt camera up in ground observer mode
GroundCamTiltDown	DOWN	Tilt camera down in ground observer mode
IncMainThrust	ADD CTRL	Increment main thrust level
DecMainThrust	SUBTRACT CTRL	Decrement main thrust level
KillMainRetroThrust	MULTIPLY	Kill main and retro thrusters
OverrideFullMainThrust	ADD	Temporarily set full main thrust
OverrideFullRetroThrust	SUBTRACT	Temporarily set full retro thrust
IncHoverThrust	NUMPAD0	Increment hover thrust level
DecHoverThrust	DECIMAL	Decrement hover thrust level
RCSEnable	DIV CTRL	Enable/disable RCS
RCSMode	DIVIDE	Rotational/translational RCS mode
RCSPitchUp	NUMPAD2	RCS pitch up
RCSPitchDown	NUMPAD8	RCS pitch down
RCSYawLeft	NUMPAD1	RCS yaw left
RCSYawRight	NUMPAD3	RCS yaw right
RCSBankLeft	NUMPAD4	RCS bank left
RCSBankRight	NUMPAD6	RCS bank right
RCSUp	NUMPAD2	RCS translate up
RCSDown	NUMPAD8	RCS translate down
RCSLeft	NUMPAD1	RCS translate left
RCSRight	NUMPAD3	RCS translate right
RCSForward	NUMPAD6	RCS translate forward
RCSBack	NUMPAD9	RCS translate backward
LPRCSPitchUp	NUMPAD2 CTRL	low power RCS pitch up
LPRCSPitchDown	NUMPAD8 CTRL	low power RCS pitch down
LPRCSYawLeft	NUMPAD1 CTRL	low power RCS yaw left
LPRCSYawRight	NUMPAD3 CTRL	low power RCS yaw right
LPRCSBankLeft	NUMPAD4 CTRL	low power RCS bank left
LPRCSBankRight	NUMPAD6 CTRL	low power RCS bank right
LPRCSUp	NUMPAD2 CTRL	low power RCS translate up
LPRCSDown	NUMPAD8 CTRL	low power RCS translate down
LPRCSLeft	NUMPAD1 CTRL	low power RCS translate left
LPRCSRight	NUMPAD3 CTRL	low power RCS translate right
LPRCSForward	NUMPAD6 CTRL	low power RCS translate forward
LPRCSBack	NUMPAD9 CTRL	low power RCS translate backward
NMHoldAltitude	A	navmode hold altitude
NMHLevel	L	navmode wings level
NMPrograde	LBRACKET	navmode prograde
NMRetrograde	RBRACKET	navmode retrograde
NMNormal	SEMICOLON	navmode orbit-normal
NMAntinormal	APOSTROPHE	navmode orbit-antinormal
NMKillrot	NUMPAD5	navmode kill rotation
Undock	D CTRL	disengage main docking port
IncElevatorTrim	DELETE	Increment elevator trim setting
DecElevatorTrim	INSERT	Decrement elevator trim setting
WheelbrakeLeft	COMMA	Apply wheel brake at left main gear
WheelbrakeRight	PERIOD	Apply wheel brake at right main gear
HUD	H CTRL	Switch HUD on/off
HUDMode	H	Cycle to next HUD mode
HUDReference	R CTRL	Select HUD reference body
HUDTarget	R CTRL ALT	Select HUD target object
HUDColour	H ALT	Cycle to next HUD colour
IncSimSpeed	T	Increment simulation speed ×10
DecSimSpeed	R	Decrement simulation speed /10
IncFOV	X	Zoom camera out
DecFOV	Z	Zoom camera in
StepIncFOV	X CTRL	Zoom camera out to next 10° step
StepDecFOV	Z CTRL	Zoom camera in to next 10° step
MainMenu	F4	Show/hide main menu
DlgHelp	F1 ALT	Open help window
DlgCamera	F1 CTRL	Open camera dialog
DlgSimSpeed	F2 CTRL	Open time acceleration dialog
DlgCustomCmd	F4 CTRL	Open custom function dialog
DlgVisualHelpers	F9 CTRL	Open visual helpers dialog
DlgRecorder	F5 CTRL	Open record/playback control dialog
DlgInfo	I CTRL	Open object info window
DlgMap	M CTRL	Open map window
DlgSelectVessel	F3	Open vessel selection dialog
SelectPrevVessel	F3 CTRL	Switch to previous focus vessel
ToggleCamInternal	F1	Switch cockpit/external view
ToggleTrackMode	F2	Cycle to next external track mode
TogglePanelMode	F8	Cycle to next cockpit mode
TogglePlanetarium	F9	Switch planetarium mode on/off
ToggleRecPlay	C CTRL	Switch recorder/playback of/off
Pause	P CTRL	Pause/resume simulation
Quicksave	S CTRL	Save current simulation state
DlgCapture	SYSRQ CTRL	Open screen capture control dialog
Quit	Q CTRL	Quit simulation session

# Mesh files
Orbiter uses a custom mesh file format. Mesh files are ASCII text files, and are by default located in the .\Meshes subdirectory, unless the MeshDir entry in the main configuration file points to a different location (see Chapter 2.1). Some objects (e.g. Vessel classes) may place their meshes into their own subdirectory below .\Meshes to keep them grouped together.
Vertex coordinates are defined in the object’s local coordinate system. Remember that Orbiter uses a left-handed coordinate system, where +x = right axis, +y = up axis, +z = forward axis. To conform with Orbiter’s default vessel orientation conventions, vessel meshes should be aligned so that the main thrust direction points to the positive z-direction, the positive x-axis points right, and the positive y-axis points up.
Vertex coordinate values are in units of meters [m].
The mesh file format is given by
MSHX1	header
GROUPS <n>	<n>: number of mesh groups
<group 1>	group spec 1
<group 2>	group spec 2
. . .
<group n>	group spec n
MATERIALS <m>	<m>: number of material definitions
<mtrl-name 1>	material name 1
<mtrl-name 2>	material name 2
. . .
<mtrl-name m>	material name m
<material 1>	material definition 1
<material 2>	material definition 2
. . .
<material m>	material definition m
TEXTURES <t>	<t>: number of texture definitions
<tex-name 1>	texture name 1
<tex-name 2>	texture name 2
<tex-name t>	texture name t
The rest of this chapter contains details about the components of the mesh file format.
## Mesh groups
Meshes are subdivided into mesh groups. Each mesh group has one material and one texture map associated with it. If you want different parts of the objects to have different material properties, the mesh must be split into groups accordingly. Mesh groups act as a rigid sub-units within the mesh for the purposes of mesh animation.
### Group specs
A mesh group specification inside the mesh file has the following format:
[LABEL <label>]	group label, optional
[MATERIAL <i>]	material index, optional
[TEXTURE <j>]	texture index, optional
[TEXWRAP <wrap>]	texture wrap mode: <wrap> = U or V or UV, optional
[NONORMAL]	“no normals” flag, see below, optional
[FLAG <f>]	multi-purpose bit flags, see below, optional
GEOM <nv> <nt>	<nv>: vertex count, <nt> triangle count
<vtx 0>	vertex spec 0
<vtx 1>	vertex spec 1
. . .
<vtx nv−1>	vertex spec nv−1
<tri 0>	triangle spec 0
<tri 1>	triangle spec 1
<tri nt−1>	triangle spec nt−1
Group components:
- A group can be assigned an optional label (tag LABEL) to make it easier to address from within the vessel module code (e.g. for coding an animation sequence). The label must be a single word without white space. A separate tool (.\Orbitersdk\Utils\meshc.exe) can be used to scan a mesh file and write out a C++ header file containing the group labels and their integer indices. This header file can then be included in the vessel module code. Make sure to re-run meshc whenever the mesh group structure changes, to keep the associations up to date.
- A material index can be used to assign a material to the group. Indices ≥ 1 assign a material from the mesh material list. Index 0 refers to the default material (white, diffuse and opaque). If the group doesn’t specify a material index, it inherits the previous group’s material. If the first mesh group does not specify a material index, index 0 is implied.
- A texture index can be used to assign a texture map to the group. Indices ≥ 1 assign a texture from the mesh texture list. Index 0 indicates “no texture”. If the group doesn’t specify a texture index, it inherits the previous group’s texture. If the first mesh group does not specify a texture index, index 0 is implied.
- The optional TEXWRAP flag defines how textures wrap around the object. “U” causes textures to wrap in the u-coordinate direction in texel space, “V” wraps in v-coordinate direction, and “UV” wraps in both directions. Default is no wrapping.
- The optional NONORMAL flag indicates that vertex definitions in this group don’t contain normal information, meaning that the first two numbers after the vertex coordinate (x,y,z) triplet are interpreted as texture coordinate (u,v) pair.
- The optional FLAG tag allows to specify a user-defined 32-bit flag whose interpretation is context-dependent. Below is a list of bit settings currently recognised by Orbiter:
Mesh type	Flag	Interpretation
Vessel	0x00000001	Do not use this group to render ground shadows
Vessel	0x00000002	Do not render this group
Vessel	0x00000004	Do not apply lighting when rendering this group
Vessel	0x00000008	Texture blending directive: additive with background

- The GEOM specification heads the vertex and triangle list for the mesh group. It specifies the lengths of both lists.
- A vertex list (see below)
- A triangle list (see below)
### Vertex list
Each group contains a vertex list, defining the positions, and optionally normal directions and texture coordinates of the vertices in the group.
Each line in the list defines a vertex and contains up to 8 floating point numbers (separated by spaces:
<x> <y> <z> [<nx> <ny> <nz>] [<tu> <tv>]
- The first 3 numbers contain the Cartesian vertex coordinates (x, y, z) in the object’s local frame of reference. Units are meters [m].
- The next 3 numbers (if present) contain the surface normal direction at the vertex location (nx, ny, nz), unless the group has the NONORMAL flag set. Orbiter needs the normal direction for lighting calculations. If no normal specification is available (or if the NONORMAL flag is present), Orbiter guesses the normal direction as the average of the normals of the adjacent triangles. This works well for smooth surfaces, but should be avoided for surfaces that contain sharp edges. Vertices located on edges require two vertex entries with different normals, referenced by the appropriate triangles. Normal definitions should be normalised: sqrt(nx2 + ny2 + nz2) = 1.
- The next 2 numbers (if present) contain the vertex texture coordinates (u, v). Texture coordinates are only required if the group uses a texture (has texture index ≥ 1). Texture coordinates define how a rectangular 2D texture is mapped onto the object surface. Texture coordinate (0, 0) refers to the lower left corner of the texture, (1, 1) refers to the upper right corner. Coordinates > 1 and < 0 are allowed and cause textures to repeat periodically.
### Triangle list
The group’s triangle list follows immediately below the vertex list. It defines the triangles which compose the group’s polygonal (piecewise flat) surface.
- Each line in the list defines a triangle and consists of 3 integer numbers (i, j, k). Each is an index referencing a vertex in the vertex list (starting from 0).
- Only the “clockwise” (CW) side of the triangle is rendered: the side which, when looked at, has the vertices arranged in a clockwise order. The opposite, “counterclockwise” (CCW) side is invisible.
- If both sides of the triangle must be rendered (e.g. if representing part of a thin plate), two triangles must be defined, one for each side.
- To flip the rendered side of a triangle (e.g. to correct for “inside out” artefacts), the vertex index order must be rearranged: (i, j, k) → (i, k, j).
## Material list
Material specifications allow specification of general light reflection and emission properties, as well as opacity values, that can be applied to mesh group surfaces. The material list consists of
- A header line, MATERIALS <m>, defining the number <m> of materials.
- A list of material names
- A list of material properties
Each material property specification consists of
- A header line, MATERIAL <name>, where <name> is an entry from the list of material names
- A line containing the diffuse reflection colour and opacity: <rd> <gd> <bd> <ad>. This is the colour that is diffusely (in all directions) reflected from an illuminated surface.
- A line containing the ambient material colour and opacity: <ra> <ga> <ba> <aa>. This is the colour of an unlit surface.
- A line containing the the specular colour, opacity and reflection characteristics: <rs> <gs> <bs> <as> [<p>]. This is the colour of light reflected by a polished surface into a narrow cone. The power entry (<p>) specifies the width of the cone into which light is reflected. Higher values represent a narrower cone, i.e. sharper reflections. Typical values are around 10. If <p> is omitted, the default value is 0.
- A line containing the emissive colour and opacity: <re> <ge> <be> <ae>. This is the colour of light emitted by a glowing surface.
For each colour specification, <r>, <g> and <b> denote the red, green and blue (RGB) colour components. <a> is the opacity. RGB values should be between 0 and 1, but can be > 1 for special effects. Opacity values must be between 0 and 1.
## Texture list
The texture list contains the names of the texture files loaded by the mesh. Textures must be in DDS (Direct Draw Surface) format. The names in the list must contain the file extension (.dds). They can contain a path specification, which is interpreted relative to Orbiter’s main Texture directory (.\Textures by default).
- A DirectX SDK tool, dxtex, which is included in the Orbiter SDK package, can be used to convert to DDS from other bitmap formats.
- Use either DXT1 compressed format (for opaque textures or textures with binary transparency) or DXT5 (for textures containing semi-transparent areas). DXT1 compresses to half the size of DXT5 but has slightly higher compression artefacts.
- Texture bitmaps should have sizes of powers of 2 for maximum compatibility (in particular with older graphics cards). Also avoid texture maps > 2048×2048 pixels.
- If a texture is to be dynamically updated during the simulation (e.g. instrument panels in virtual cockpits) the texture name in the list should be followed by the flag ‘D’. Orbiter decompresses these surfaces on loading to allow more efficient dynamic updates.
## Performance optimisation
Complex meshes can improve the visual appearance of the object they represent, but they also impose a computational cost on the render engine, leading to lower simulation frame rates and less fluid animation. It can also potentially lead to a loss of accuracy in the trajectory calculation. A balance between visualisation quality and simulation performance should be kept in mind. There are a few ways to optimise the mesh structure to improve performance:
- Mesh groups using the same texture should be listed in sequence in the mesh. Unnecessary switching between textures can degrade performance if textures must be swapped in and out of video memory.
- Within a sequence of groups using the same texture, groups using the same material should be kept together for the same reason.
- Avoid large numbers of very small groups. If small mesh groups use the same texture and material parameters, and are not animated individually, consider merging them into a single group.
- To avoid visual artefacts, groups using transparent textures or materials should be sorted to the end of the mesh. If transparent groups overlap, the innermost ones should be listed before the outer ones.
  In order to render transparency correctly, DirectX requires the scene seen through the transparent surfaces to be fully built before the transparent part itself is rendered. Any objects rendered after the transparent part can be obscured by it (z-buffering artefact).
- Surfaces with transparency and specular reflection are more expensive to render than opaque and diffusive surfaces.
- And most importantly: Keep the vertex count reasonably low!
## Mesh converters
To convert an existing model in a standard mesh format to an Orbiter mesh, check the Orbiter web forum for mesh converters created by other users. There is currently a converter which converts from Truespace asc format, which many 3D editors can export. If you have written your own mesh editor or converter, publish it!
## Mesh utilities
The Orbiter SDK contains a few utilities that help to extract data from mesh files. They are located in the Orbitersdk\utils folder.
- shipedit.exe: Extracts geometric information from a mesh that is useful for setting up the physical vessel parameters in its configuration file or module code. These include the mesh bounding box, volume, cross-sectional areas, and inertia tensor assuming a homogeneous density distribution.
- meshc.exe: Mesh compiler. Currently, this extracts mesh parameters and group labels into a C++ header file that can be included by the vessel code for convenient access to named mesh groups, e.g. to address them for animations and dynamic material updates.